## Slide 1: C3D to FBX Conversion Tool
Bridging Clinical Motion Capture & Interactive Visualization • Endless Games and Learning Lab • James Sypherd

## Slide 2
THE CLINICAL GAP
Clinical data collected — never visualized
Rich biomechanical data sits in .C3D files. Patients never see it.
Patients see numbers, not movement
Charts and spreadsheets don't build intuition or drive motivation.
50% compliance drop after 2 weeks
Without engaging feedback, patients abandon home exercise programs.
Existing software: $100,000+
Vicon, Qualisys — research-grade cost, unreachable for most PT clinics.
No interactive gamification layer
The motion capture hardware exists. The game engine bridge does not.

## Slide 3
THE PIPELINE
📡
C3D File
Binary clinical format (Vicon/Nexus)
▶
🔍
Inspect +Validate
inspect_c3d.py Label discovery Marker mapping
▶
🧮
Solve
solve_csv_to _ue_rigjson.py Forward kinematics
▶
🦴
Rig + Animate
blender_virtual _csv_to_fbx.py Mixamo skeleton
▶
🎮
FBX → UE5
Retarget to Mannequin / MetaHuman
Real clinical data included: t7updated2_1111111_2022_01_03_barewalk1.c3d (ASU biomechanics lab gait session)
Key innovation: Mixamo-named skeleton → drops into UE5 / Unity retargeting with ZERO manual rigging
Vicon Nexus 3D viewport — full-body skeleton reconstruction with force plates active (ASU biomechanics lab)

## Slide 4
CODE SPOTLIGHT 1 — inspect_c3d.py
Lab-agnostic label discovery
Problem: Every mocap lab names markers differently. Vicon uses LSHO; another lab uses LeftShoulder. This tool auto-discovers what's usable.
# Load C3D binary via ezc3d
c3d = ezc3d.c3d(path)
point_labels = c3d['parameters']
['POINT']['LABELS']['value']
# Fuzzy-match upper body markers
upper_keywords = [
"C7","CLAV","SHO","ELB","WRI",
"HEAD","FHEA","V_","JC"
]
# Smart filter: exclude lower-body false hits
lower_only = ['KNEE','ANKLE','TOE']
# Output: spec list for downstream scripts
# Example: ('LSHO', ['LSHO'], None),
68 markers reconstructed (60 physical + 8 virtual)

## Slide 5
CODE SPOTLIGHT 2 — Quaternion Solver
solve_csv_to_ue_rigjson.py
Converts marker positions → 23-joint rotations using forward kinematics, hemisphere continuity, and delta quaternions
# Build rotation from aim + roll pole
def frame_from_aim_pole(aim, pole):
y = norm(aim)
z = pole - dot(pole,y)*y
x = norm(cross(y, z))
return stack([x,y,z], axis=1)
# CRITICAL: Prevent 180° flip artifacts
def pole_continuous(pole, prev):
if dot(pole, prev) < 0.0:
return -pole # flip fix
return pole
# Delta relative to REST pose
# Prevents double-rotation in Blender
delta = mul_quat(inv_quat(rest),
local_quat[f])
3 HARD PROBLEMS SOLVED
① Quaternion flips
Mocap noise causes 180° sign
flips — hemisphere continuity
check eliminates popping.
② Double rotation
Delta quats relative to rest
pose prevent error accumulation.
③ Torso listing
Global correction matrix at
calibration frame removes
constant lean/drift.

## Slide 6
CODE SPOTLIGHT 3 — Skeletal Rigging
blender_virtual_csv_legs_to_fbx.py
Auto-builds patient-specific Mixamo skeleton from real bone measurements, smooth warm-up blend from T-pose to motion
# Measure REAL bone lengths from data
thigh_l = (fr0['VLHI']-fr0['VLKN']).length
calf_l = (fr0['VLKN']-fr0['VLAN']).length
# Build T-pose with Mixamo names
# (UE5 retarget works immediately)
add_bone("mixamorig:LeftUpLeg",
lhip, lhip+Vector((0,0,-thigh_l)),
parent="mixamorig:Hips")
# Warm-up blend: T-pose → stable motion
# 24 frames @ 120fps = 0.2s smooth entry
for i in range(WARMUP_BLEND_FRAMES):
t = i / float(WARMUP_BLEND_FRAMES)
pb.rotation_quaternion =
q0.slerp(target_rot, t)
ENGINEERING DECISIONS
Patient-specific sizing
Bones measured from each
patient's actual data — not a
generic template skeleton.
Mixamo naming = free retarget
Works with UE5 Mannequin,
MetaHuman, any Mixamo char.
24-frame warm-up blend
Smooth T-pose → motion entry.
No jarring first-frame artifacts.

## Slide 7
LIVE DEMO — No Motion Capture Hardware Required
STEP 1
Open Real Clinical Data
Load barewalk1.c3d — actual ASU patient gait session. Real markers, real kinematics, real clinical context.
[ Nexus / UE5 screenshot ]
STEP 2
Run Pipeline Live
python inspect_c3d.py → auto-discovers markers Convert to virtual_joints.csv in real time.
[ Nexus / UE5 screenshot ]
STEP 3
Blender Headless Export
blender --background --python blender_virtual... FBX exports in under 30 seconds on any laptop.
[ Nexus / UE5 screenshot ]
STEP 4
UE5 Viewport
Import FBX → retarget to Mannequin → Press Play. Patient walks across screen. Zero manual rigging.
[ Nexus / UE5 screenshot ]
STEP 5
Gamification Mockup
Rep counter, form score, streak system. Patient sees their own movement pattern, gamified.
[ Nexus / UE5 screenshot ]

## Slide 8
MARKET OPPORTUNITY
$45B+
US Physical Therapy Market
50%
Compliance Drop After 2 Weeks
30–60%
Adherence Increase With Gamification
$99/mo
Target Clinic Price vs. $100K+ Incumbents
WHY NOW
• Consumer VR is mainstream — Apple Vision Pro, Meta Quest 3
• Post-COVID telehealth accelerated remote PT adoption
• UE5 MetaHuman = photorealistic patient avatars, out of the box
• AI-driven form analysis is commercially viable at low cost

## Slide 9
DEVELOPMENT ROADMAP
MVP 4 Weeks
✓ C3D → FBX pipeline (this tool)
✓ Real-time UE5 skeleton preview
✓ Rep counter + ROM scoring
✓ Single exercise type: gait
Beta 8 Weeks
✓ Clinic onboarding portal
✓ Multi-exercise library
✓ Patient progress dashboard
✓ AI form coaching overlays
V1.0 12 Weeks
✓ Mobile companion app
✓ Cloud processing API
✓ EMR/EHR integration
✓ VR mode (Quest 3 / Vision Pro)

## Slide 10
ENDLESS GAMES AND LEARNING LAB
The data already exists.
We built the bridge.
C3D → FBX → Unreal Engine → Patient sees their movement in 3D, scored in real time.
Request a Live Demo
github.com/BetterCodeGoblin
James Sypherd · sypherdj1@gmail.com · ASU